; Contact: ; Trevor Dorchies Kristin Starnes ; . Dodge Announces Police Pursuit Version of 2018 Durango May 10, 2018, Auburn Hills, Mich. - Dodge is expanding its police vehicle lineup, adding a new Pursuit version of its Dodge Durango. “Unofficial testing results at the Michigan State Police 2018 model-year vehicle evaluation event created such a stir among law enforcement agencies that we simply had to find a way to build this vehicle,” said Steve Beahm, Head of Passenger Car Brands, Dodge//SRT, Chrysler and FIAT – FCA North America. “The Dodge Durango is already known as the Charger of SUVs, so it is only natural that the new Durango Pursuit complements the Charger Pursuit in police fleets across the country.” The 2018 Dodge Durango Pursuit is powered by the legendary 5.7L HEMI® V-8, coupled with a full-time, active all-wheel-drive (AWD) system. This is the same powertrain combination most commonly deployed in the Dodge Charger Pursuit, the top-selling police sedan in the U.S. market. The Durango Pursuit also offers a two-speed transfer case for true low-range off-road capability and incorporates larger, heavy-duty anti-lock brakes that deliver a 60-0 mile per hour (mph) stopping distance of 134 feet. Other notable standard features of the 2018 Dodge Durango Pursuit include: 5.7L V-8 HEMI with Fuel Saver Technology delivers best-in-class horsepower (360) and torque (390 lb.-ft.) Eight-speed automatic transmission delivers quick shifts and improved fuel economy Rear-wheel-drive-based drivetrain is the foundation for Durango’s outstanding on-road driving performance. Standard AWD further enhances driver confidence by leveraging the SUV’s 50/50 weight distribution Segment’s longest wheelbase (119.8 inches) provides added stability and improved handling Best-in-class 7,200 lb. towing capability 8.1 inches of ground clearance ParkView® rear backup camera with ParkSense® alert Eight-way power adjusting driver seat controls Air conditioning with air filtration Under-vehicle mount for spare tire, maximizing interior cargo space and accessibility Class-exclusive, K-9 friendly Tri-Zone interior temperature control Trailer sway control Spot lamp wiring prep package 220-amp alternator 800 cold cranking amp (CCA) battery Heavy-duty oil cooler and water pump Power locking fuel filler door The new 2018 Dodge Durango Pursuit V-8 AWD is available for order for a limited time. For more information, law enforcement agencies should call (800) 999-3533. Dodge//SRT For more than 100 years, the Dodge brand has carried on the spirit of brothers John and Horace Dodge. Their influence continues today as Dodge shifts into high gear with a lineup that delivers unrivaled performance in each of the segments in which the brand competes while moving forward to a future that includes electrified muscle in the form of the next-generation, all-new Dodge Charger. The next-generation Dodge Charger electrifies a legend, with the Charger retaining its title as the world’s quickest and most powerful muscle car led by the all-new, all-electric 2024 Dodge Charger Daytona Scat Pack. The all-new Dodge Charger will also offer performance choices via multi-energy powertrain options including the 550-horsepower Dodge Charger SIXPACK H.O., powered by the 3.0L Twin Turbo Hurricane High Output engine. Dodge also keeps its foot on the gas as a pure performance brand with the 710-horsepower Dodge Durango SRT Hellcat, the most powerful SUV ever, and best-in-class standard performance in the compact utility vehicle segment with the Dodge Hornet. Dodge is part of the portfolio of brands offered by leading global automaker and mobility provider Stellantis. For more information regarding Stellantis (NYSE: STLA), please visit www.stellantis.com. Follow Dodge//SRT and company news and video on: Company blog: http://blog.stellantisnorthamerica.com Media website: http://media.stellantisnorthamerica.com Dodge brand: www.dodge.com Direct Connection: www.DCPerformance.com DodgeGarage: www.dodgegarage.com Facebook: www.facebook.com/dodge Instagram: www.instagram.com/dodgeofficial Twitter: www.twitter.com/dodge and @StellantisNA YouTube: www.youtube.com/dodge, https://www.youtube.com/StellantisNA ; .

-###- Additional information and news from Stellantis are available at https://media.stellantisnorthamerica.com.